## Slide 1: Android TIF Introduction
By Chen Changhong

## Slide 2: TV Input Framework Architecture
https://source.android.com/devices/tv/

## Slide 3: Flow

## Slide 4: TV App
TvApp
TvView
mSurface
TvInputManagerHelper
TvInputManager
TvInputManagerService
IPC
TvInputCallback
TV Provider
TvContract
mSession

## Slide 5: TV App
/packages/apps/TV/src/com/android/tv/TvActivity.java
/packages/apps/TV/src/com/android/tv/MainActivity.java
一个和用户交互的系统应用
Applications talk to the TV input manager to list TV inputs and check their status.
Once an application find the input to use, it uses TvView or TvRecordingClient for further interaction such as watching and recording

## Slide 6: TV App
Setup and configuration
  Auto-detect TV Inputs
  Let TV Inputs initiate channel setup
  Control parental settings
  Edit channels
Viewing
  Access and navigate all TV channels
  Access TV program information bar
  EPG
  Support multiple audio and subtitle tracks

## Slide 7: TV App
void onCreate()
  mTvView = (TunableTvView) findViewById(R.id.main_tunable_tv_view)
  mTvView.initialize(…)
  mTvInputManagerHelper = tvApplication.getTvInputManagerHelper()
void startTV()
  TunableTvView.java
  mTvView.start(mTvInputManagerHelper);

## Slide 8: TvView
/frameworks/base/media/java/android/media/tv/TvView.java
Displays TV contents.
Provides a high level interface for applications to show TV programs from various TV sources that implement TvInputService
surface用于显示视频播放的内容
session可以控制音量的大小等
Dispatch key event, touch event etc. to Session

## Slide 9: TV Provider
  /packages/providers/TvProvider/src/com/android/providers/tv/TvProvider.java
  The TV Provider database stores the channels and programs from TV Inputs
  Passthrough TV inputs do not store channels and programs.

## Slide 10: TvContract
/frameworks/base/media/java/android/media/tv/TvContract.java
The contract between the TV provider and applications. Contains definitions for the supported URIs and columns
TvContract.Channels 频道列表
TvContract.Programs 频道里面的节目单

## Slide 11: TvInputManagerHelper
Implement TvInputCallback to get TvInput event
  TvInputCallback mInternalCallback = new TvInputCallback(){…}
  onInputXXX(){
    for (callback : mCallbacks)
    callback.onInputStateChanged(inputId, state)
  }
mCallbacks
  addCallback/removeCallback
Get TvInputManager and register Callback
  mTvInputManager = (TvInputManager) context.getSystemService(Context.TV_INPUT_SERVICE)
  mTvInputManager.registerCallback(mInternalCallback, mHandler)

## Slide 12: TVInputManager
/frameworks/base/media/java/android/media/tv/TvInputManager.java
Central system API to the overall Framework, which arbitrates interaction between applications and the selected TV inputs.
获取TvInputManager
  TvInputManager tvInputManager =(TvInputManager) getSystemService(Context.TV_INPUT_SERVICE)

## Slide 13: TvInputCallback
/frameworks/base/media/java/android/media/tv/TvInputManager.java
Callback used to monitor status of the TV inputs
  onInputStateChanged()
  onInputAdded()
  onInputRemoved()
  onInputUpdated()
  onTvInputInfoUpdated()
Usage
  /packages/apps/TV/src/com/android/tv/MainActivity.java
  mTvInputManagerHelper.addCallback(mTvInputCallback);

## Slide 14: TvInputManager
获取Input list
  List<TvInputInfo> list = tvInputManager.getTvInputList(); for(TvInputInfo info:list)
  {
  Log.i(TAG, "id:" + info.getId());
  }
Result
  id:com.mediatek.tvinput/.component.ComponentInputService/HW1 id:com.mediatek.tvinput/.dtv.TunerInputService/HW0 id:com.mediatek.tvinput/.composite.CompositeInputService/HW2 id:lenovo.com.ismartvlive/.Ismartvliveservice

## Slide 15: TvInputManager
void tune(Uri channelUri, Bundle params)
  Called by TvView.tune()
    Called by TvViewSession.tune()
      Called by MainActivity.tune()
  Call mService.tune() //ITvInputManager mService
  ITVInputManager Service register
    SystemServiceRegistry.java
    IBinder iBinder = ServiceManager.getServiceOrThrow(Context.TV_INPUT_SERVICE);
    ITvInputManager service = ITvInputManager.Stub.asInterface(iBinder);
    return new TvInputManager(service, UserHandle.myUserId());

## Slide 16: TvInputManagerService
TvInputManagerService
TvInputHardwareManager
TvInputService
TvInputService
HardwareListener

## Slide 17: TvInputManagerService
/frameworks/base/services/core/java/com/android/server/tv/TvInputManagerService.java
provides a system service that manages television inputs
mTvInputHardwareManager = new TvInputHardwareManager(context, new HardwareListener());

## Slide 18: TvInputHardwareManager
/frameworks/base/services/core/java/com/android/server/tv/TvInputHardwareManager.java
helper class for TvInputManagerService to handle TV input hardware
basic connection management and forwarding calls to TvInputHal which eventually calls to tv_input HAL module.
  TvInputHal mHal = new TvInputHal(this);
  IHdmiHotplugEventListener mHdmiHotplugEventListener =
  new HdmiHotplugEventListener()
  onDeviceAvailable()
  onDeviceUnavailable()

## Slide 19: TvInputService
TvInputService
TvInputService.Session
Passthrough Input
Tuner Input
3rd Party Input

## Slide 20: TvInputService
/frameworks/base/media/java/android/media/tv/TvInputService.java
实现onCreatSession()方法返回一个TvInputService.Session对象
例子实现
  定义/developers/build/prebuilts/androidtv/sample-inputs/app/src/main/AndroidManifest.xml
  实现/developers/build/prebuilts/androidtv/sample-inputs/app/src/main/java/com/example/android/sampletvinput/rich/RichTvInputService.java

## Slide 21: TvInputService.Session
TvView通过Tune方法来播放指定的节目,
调用Session的onTune(Uri channelUri)方法来播放uri中的节目
onSetSurface()方法来设置播放的surface

## Slide 22: TV Input
TV Input
  可以看做是一个代表物理或者虚拟的电视接收器或者输入端口的应用。Input在TIF中可以看做是一个输入源
Implement TvInputService
an input source of TV, which can be a pass-through input such as HDMI, or a tuner input which provides broadcast TV programs.
The system binds to the TV input per application’s request. on implementing TV inputs.

## Slide 23: Passthrough input
Some inputs, like the HDMI input can be provided only by the manufacturer as they speak directly with the underlying hardware.
Notes: To obtain the URI used to reference the passthrough input, use the android.media.tv.TvContract utility method buildChannelUriForPassthroughInput(String inputId). The TV App communicates with the TV Input Manager to reach the HDMI TV Input.

## Slide 24: Built-in tuner
In this example, the Built-in Tuner TV Input provided by the device manufacturer is trusted and has full access to the TV Provider.

## Slide 25: Third-party input
the external STB TV Input is provided by a third party. Since that TV Input can’t directly access the HDMI video feed coming in, it must go through the TV Input Manager and use the HDMI TV Input provided by the device manufacture.
Notes: Through the TV Input Manager, the external STB TV Input can speak with the HDMI TV Input and ask it to show the video on HDMI1. So the STB TV Input can control the TV while the manufacturer-provided HDMI TV Input renders the video.

## Slide 26
TvInput
TvInputInfo
TvInputHal.java
TvInputHal(Native)
TV Input HAL Module

## Slide 27: TvInputInfo
/frameworks/base/media/java/android/media/tv/TvInputInfo.java
specify meta information of a TV input
  Type(Tuner/Composite/Svideo/HDMI/….)
  Label
  Icon

## Slide 28: TvInputHal(Java)
/frameworks/base/services/core/java/com/android/server/tv/TvInputHal.java
Provides access to the low-level TV input hardware abstraction layer
Call Native Function
  nativeOpen
  nativeAddOrUpdateStream
  nativeRemoveStream
  nativeGetStreamConfigs
  nativeClose
Called by Native function
  onDeviceAvailabledevice ()
  onDeviceUnavailable
  onStreamConfigurationChanged
  onFirstFrameCaptured

## Slide 29: TvInputHal(Native)
/frameworks/base/services/core/jni/com_android_server_tv_TvInputHal.cpp
register_android_server_tv_TvInputHal()
Class JTvInputHal
nativeOpen
  JTvInputHal::createInstance()
    sp<ITvInput> tvInput = ITvInput::getService()
    return new JTvInputHal(env, thiz, tvInput, looper))
nativeAddOrUpdateStream
  tvInputHanl->addOrUpdteStream(deviceId, streamId, surface)
    mTvInput->getStreamConfigurations()
    mTvInput->openStream(deviceId, streamId)

## Slide 30: TV Input HAL Module
TV Input HAL
  tv_input module
  TV Input的硬件抽象层，可以让系统的TV inputs访问TV特有硬件

## Slide 31: TV Input Skeleton
/hardware/interfaces/tv/input/1.0/default/TvInput.cpp
/hardware/interfaces/tv/input/1.0/default/TvInput.h
struct TvInput : public ITvInput
{
}

## Slide 32: TV HAL module skeleton
/hardware/libhardware/modules/tv_input/tv_input.cpp
/hardware/libhardware/include/hardware/tv_input.h
tv_input_module_t
  .methods = &tv_input_module_methods
tv_input_module_methods =
  // return hw_device_t of tv_input_private_t
  .open = tv_input_device_open
tv_input_private_t
  tv_input_device_t device
    struct hw_device_t common
    int (*initialize)(..)
    int (*get_stream_configurations)(…)
    int (*open_stream)(…)
  const tv_input_callback_ops_t* callback

## Slide 33: Another Example
https://github.com/songwenju/TIFSample